10A NCAC 15 .1602	IMPLEMENTATION

10A NCAC 15 .1603	RADIATION PROTECTION PROGRAMS

10A NCAC 15 .1604	OCCUPATIONAL DOSE LIMITS FOR ADULTS

10A NCAC 15 .1605	REQUIREMENTS FOR SUMMATION OF EXTERNAL, INTERNAL DOSES

10A NCAC 15 .1606	EXTERNAL DOSE FROM AIRBORNE RADIOACTIVE MATERIAL

10A NCAC 15 .1607	DETERMINATION OF INTERNAL EXPOSURE

10A NCAC 15 .1608	PLANNED SPECIAL EXPOSURES

10A NCAC 15 .1609	OCCUPATIONAL DOSE LIMITS FOR MINORS

10a ncac 15 .1610	DOSE EQUIVALENT TO AN EMBRYO/FETUS

10A NCAC 15 .1611	DOSE LIMITS FOR INDIVIDUAL MEMBERS OF THE PUBLIC

10A NCAC 15 .1612	COMPLIANCE WITH DOSE LIMITS FOR MEMBERS OF THE PUBLIC

10a ncac 15 .1613	SURVEYS

10A NCAC 15 .1614	MONITORING OF EXTERNAL AND INTERNAL OCCUPATIONAL DOSE

10A NCAC 15 .1615	CONTROL OF ACCESS TO HIGH RADIATION AREAS

10A NCAC 15 .1616	CONTROL OF ACCESS TO VERY HIGH RADIATION AREAS

10A NCAC 15 .1617	ACCESS TO VERY HIGH RADIATION AREAS: IRRADIATORS

10A NCAC 15 .1618	USE OF PROCESS OR OTHER ENGINEERING CONTROLS

10A NCAC 15 .1619	USE OF OTHER CONTROLS TO RESTRICT INTERNAL EXPOSURE

10A NCAC 15 .1620	USE OF INDIVIDUAL RESPIRATORY PROTECTION EQUIPMENT

10A NCAC 15 .1621	RESTRICTIONS ON THE USE OF RESPIRATORY PROTECTION EQUIPMENT

10A NCAC 15 .1622	SECURITY OF SOURCES OF RADIATION

10A NCAC 15 .1623	CAUTION SIGNS

10A NCAC 15 .1624	POSTING REQUIREMENTS

10A NCAC 15 .1625	EXCEPTIONS TO POSTING REQUIREMENTS

10A NCAC 15 .1626	LABELING REQUIREMENTS AND EXEMPTIONS

10A NCAC 15 .1627	PROCEDURES FOR RECEIVING AND OPENING PACKAGES

10A NCAC 15 .1628	GENERAL REQUIREMENTS FOR WASTE DISPOSAL

10A NCAC 15 .1629	METHOD FOR OBTAINING APPROVAL OF DISPOSAL PROCEDURES

10A NCAC 15 .1630	DISPOSAL BY RELEASE INTO SANITARY SEWERAGE

10A NCAC 15 .1631	TREATMENT OR DISPOSAL BY INCINERATION

10A NCAC 15 .1632	DISPOSAL OF SPECIFIC WASTES

10A NCAC 15 .1633	TRANSFER FOR DISPOSAL AND MANIFESTS

10A NCAC 15 .1634	COMPLIANCE WITH ENV. AND HEALTH PROTECTION REGULATIONS

10A NCAC 15 .1635	GENERAL PROVISIONS FOR RECORDS

10A NCAC 15 .1636	RECORDS OF RADIATION PROTECTION PROGRAMS

10A NCAC 15 .1637	RECORDS OF SURVEYS

10A NCAC 15 .1638	DETERMINATION OF PRIOR OCCUPATIONAL DOSE

10A NCAC 15 .1639	RECORDS OF PLANNED EXPOSURES

10A NCAC 15 .1640	RECORDS OF INDIVIDUAL MONITORING RESULTS

10A NCAC 15 .1641	RECORDS OF DOSE TO INDIVIDUAL MEMBERS OF THE PUBLIC

10A NCAC 15 .1642	RECORDS OF WASTE DISPOSAL

10A NCAC 15 .1643	RECORDS OF TESTING ENTRY CONTROL DEVICES

10A NCAC 15 .1644	FORM OF RECORDS

10A NCAC 15 .1645	REPORTS OF THEFT OR LOSS OF LICENSED RADIOACTIVE MATERIAL

10A NCAC 15 .1646	NOTIFICATION OF INCIDENTS

10A NCAC 15 .1647	REPORTS OF RADIATION EXCEEDING THE LIMITS

10A NCAC 15 .1648	REPORTS OF PLANNED SPECIAL EXPOSURES

10A NCAC 15 .1649	REPORTS OF INDIVIDUAL MONITORING

History Note:	Authority G.S. 104E-7(a)(2); 104E-7(a)(3); 104E-7(a)(5); 104E-12; 104E-12(a); 104E-15; 10 C.F.R. Chapter 1, Commission Notices, Policy Statements, Agreement States, 46 F.R 7540;

Eff. January 1, 1994;

Temporary Amendment Eff. August 20, 1994 for a period of 180 days or until the permanent rule becomes effective, whichever is sooner;

Amended Eff. October 1, 2013; November 1, 2007; May 1, 2006; January 1. 2005; August 1, 2002; April 1, 1999; August 1, 1998; May 1, 1995;

Transferred and Recodified from 15A NCAC 11 .1602 - .1649 Eff. February 1, 2015;

Amended Eff. March 1, 2017;

Repealed Eff. October 1, 2023.