15A NCAC 05H .1624	WELL STIMULATION REPORT

(a)  Within 30 calendar days after the conclusion of stimulation operations on an oil or gas well, the permittee shall submit Form 18 – Well Stimulation Report to the Department that includes the following information:

(1)	the permittee's name, address, telephone number, fax number, and email address;

(2)	the county and nearest city or town where the oil or gas well is located;

(3)	the property street address, or nearest address to the ingress and egress point leading from a public road to the well pad;

(4)	the API number, the lease name, and the oil or gas well name and number;

(5)	the type of oil or gas well;

(6)	the total volume of the base fluid;

(7)	the total volume of reused water, alternative water, freshwater, or other base fluid that was used in each hydraulic fracturing stage;

(8)	the maximum pump pressure measured at the surface during each stage of the hydraulic fracturing operations;

(9)	the types and volumes of the well stimulation fluid and proppant used for each stage of the well stimulation operations;

(10)	the well stimulation treatment data collected in accordance Rule .1613 of this Section;

(11)	for hydraulic fracture stimulations, the estimated maximum fracture height and length and estimated true vertical depth to the top of the fracture achieved during well stimulation treatments as determined by a three dimensional model using true treating pressures and other data collected during the hydraulic fracturing treatments;

(12)	the well shooting or perforation record detailing the true vertical and measured depths, and total number of shots in the wellbore;

(13)	the wellbore diagram that includes casing and cement data, perforations, and a stimulation summary;

(14)	the initial oil or gas well test information recording daily gas, oil, and water rate, and tubing and casing pressure in accordance with Rule .2201 of this Subchapter;

(15)	the initial gas analysis, performed by a laboratory certified by the State in accordance with 15A NCAC 02H .0800, which is incorporated by reference including subsequent amendments and editions; and

(16)	the engines used on-site during exploration and development, including:

(A)	the number of engines with capacities (maximum site-rated horsepower) less than 750 horsepower by engine type, such as compression ignition, two stroke lean burn ignition, four stroke lean burn ignition, rich burn spark ignition;

(B)	the number of engines with capacities (maximum site-rated horsepower) greater than or equal to 750 horsepower by engine type, such as compression ignition, two stroke lean burn ignition, four stroke lean burn ignition, rich burn spark ignition; and

(C)	the average number of hours of operation for engines in each of the categories above.

(b)  The permittee may attach to the completed Form 18 – Well Stimulation Report any information received from a service company regarding the well stimulation operations, as used in the normal course of business, to satisfy some or all of the requirements in this Rule.

History Note:	Authority G.S. 113-391(a)(5); 113-391(a)(10); 113-391(a)(11); 113-391(b); 113-391(b1);

Eff. March 17, 2015.