21 NCAC 28B .0508	WALLS

(a)  When installing retaining walls, the licensed contractor shall:

(1)	Adhere to all pertinent codes;

(2)	Adhere to all NC Department of Insurance requirements regarding the construction of retaining walls which are hereby incorporated by reference and can be found at www.ncosfm.gov/codes free of charge;

(3)	Adhere to manufacturer's or design professionals specifications;

(4)	Bury the first course of a retaining wall;

(5)	Not construct dry-laid stone walls of a height more than 3 feet above grade;

(6)	Include a subdrain system that is constructed and sized to release the subsurface water behind the wall and not allow hydrostatic pressure to build behind the wall;

(7)	Construct on a level, well-compacted base of granular material at least 6 inches deep;

(8)	Place backfill behind retaining walls in lifts no greater than 6 inches before compacted (each lift shall be well-compacted);

(9)	Prevent excessive runoff from passing over a retaining wall;

(10)	Construct vertically-set timber walls with above-ground heights equal to or less than the depth of timbers below grade;

(11)	Install deadmen every fourth course on 8 feet centers when constructing horizontally-set timber retaining walls with staggered joints;

(12)	Stagger the joints when constructing dry-laid stone walls. If successive vertical joints occur, the licensed contractor shall avoid running vertical joints more than two courses; and

(13)	Assure that segmental walls meet the manufacturer's specifications.

(b)  When installing retaining walls of dry-laid stone or concrete rubble, the licensed contractor shall:

(1)	Construct the wall no higher than 3 feet above grade; and

(2)	Stagger the joints when constructing a dry-laid stone wall.

(c)  When installing freestanding walls, the licensed contractor shall:

(1)	Install footings for masonry and cast-in-place concrete freestanding walls of reinforced concrete. The top of the footing shall be at least 1 foot below grade.

(2)	Reinforce freestanding walls as needed to prevent displacement from wind loads.

(3)	Ensure that moisture is prevented from entering a cavity wall during construction.

(4)	Ensure that segmental wall construction meets segmental wall manufacturer's specifications.

History Note:	Authority G.S. 89D-15(2); 89D-15(16);

Temporary Adoption Eff. January 1, 2016;

Eff. September 1, 2016;

Amended Eff. July 1, 2021.